# Using EXPANSION MANAGER with Tyros 5

Firstly, you must download, install and launch the Yamaha Expansion Manager Software. You can download this file by clicking HERE – Select Mac or PC version. The software runs the same on both platforms.

To be able to create a pack, your UVN files must be saved as a library. If you have sold your Tyros 4 and don’t have the ability to create a UVI (library) file, you can use this program to create a UVI file.
This is 3rd party software that runs using Java, we accept no responsibility for the use of the software or any loss of data. UVI_Creator.jar

STEP 1

Firstly we need to export the instrument information from your Tyros 5.
This information tells Expansion manager all of the information about your keyboard and links the two together.

To Export Instrument Info firstly press FUNCTION button

Once you have pressed FUNCTION you will see this screen – Now select UTILITY

Now you will see the UTILITY screen. On the left hand side you see EXPORT INSTRUMENT INFO.
Press this button.

The screen will now show you that the Information has been sent to the USB stick that you inserted.
Press OK and remove the USB stick now. Place the USB Into your Mac or PC.

We will now leave Tyros 5 for a short time and move to the PC. Open the Yamaha Expansion Manager software and you will see this opening screen for the first time.

On the left you will see the words INSTALL TARGET – this means in simple English “Your Instruments” and this is where your Tyros will appear after we have given the software information about your Tyros 5.

Now we need to tell the software about your instrument and to to do that we press the {+} sign which is next to the words Install Target. Press this + sign and the next screen will appear

This is now asking you to select the USB stick you have inserted. Here you can see that we have chosen our USB stick and the file that contains the information about our tyros is shown on the right. Click on this file and choose OPEN. This will now tell Expansion Manager everything it needs to know about your Tyros 5. You will now see the following Screen with a Tyros 5 highlighted in Purple. This is YOUR instrument!

That is the fiddly part complete. Now we can start to add sounds to the instrument.
Now this software allows you to load and convert Tyros 4 packs into your Tyros 5 – and this is how you load sounds into Tyros 5. Tyros 4 packs work with Tyros 5 and the following steps will do that.

STEP 2

Now put the USB stick of the pack you want to use into your PC, in this case we are using our Yorkshire Brass soundpack.  Now click on My Packs and click on the + sign which while show the message “Import Pack”.

We now want to tell the PC that we want to use the USB stick that we have put into the PC called Yorkshire Brass. So navigate to your USB stick and you will see this screen appear.

This shows our USB stick and the file called Yorkshire Brass – open this file and you will see a UVI file appear (see below YorkshireBrass.T105.UVI) – select this file and click open.

The Expansion Manager software will now start converting the files to work with Tyros 5 and the following screen will appear.

When this process has completed, you will see the following screen

Now the pack will appear in your pack list. Don’t worry, we are nearly finished, just a few more steps left.
The screen below is what you will now see – Yorkshire Brass is now in your available pack list.

We now want to put these voices into your Tyros 5. Insert a Blank USB stick into your PC or Mac.

Now click on the picture of the big folder that says “Yorkshire Brass” on it – a big green TICK will appear in the bottom right hand side of the folder. This tells you that the pack will be added to your Tyros 5.
At this point, if you click on the list of sounds at the lower part of the screen, you can actually select which voices you want to add. This is the benefit to using this method and allows you to use the voices you like and leave off the voices you don’t.
For the purpose of this exercise, we are going to load all of the voices.

So you can see the big green tick on the pack list above. Just at the top of the page you can see a button that says “SAVE TO USB MEMORY” when we click this button we will start to save the sounds to the USB stick that you have put into the PC or MAC. This will be the pack that we then load into your tyros 5.

CLICK ON THIS BUTTON NOW.

Now the PC will ask where you want to save the pack for your Tyros 5 – Well of course we want to save it on the Blank USB that you have put into your PC – so select the USB and now you can give the pack a name – if you are loading just one pack, call it YORKSHIRE BRASS, or if you are loading more than one pack, call it something meaningful like “Orchestral Sounds” or “Synth”.

Click on SAVE and a pack will be saved.

Whilst your PC is saving the pack, this is the screen you will see – Remember, if you are saving lots of voices it could take a while,
so be patient and don’t turn off the computer.
When the computer has finished, you will see the following screen:

This is the final process and you can now remove the USB from your computer, we are now ready to load into your Tyros.

FINAL STEP – PHEW!
Insert the USB stick into your Tyros 5, press FUNCTION button

Now select Pack Installation.

Your pack that you created on your PC will now appear, here we called ours “PACK 1″ and here it is!
Press the button next to Pack one.

You will now be asked if you want to load this pack. By pressing OK the Tyros 5 will check the files and then ask you one final time to press OK. Loading the pack will take anything from 15 minutes up to an hour depending on the number of files that you want to load.

That’s it… Well now you deserve a stiff drink or cup of coffee. The initial setting up of your Tyros is done and you don’t need to do this again. To add a new pack, simply work from STEP 2 in this guide and select all of the packs you want to install.

Here are a few things to note:

Adding packs to tyros5 is different to Tyros4 in that when you load a pack, the packs that are on the instrument are deleted, so you don’t just add one pack, you need to load ALL of the packs that you want every single time. This is a massive pain, as it means adding or taking away takes a long time, but once the packs are loaded, they are there until you add another pack.
You of course MUST have the memory board added to Tyros5 otherwise you cannot add voices at all.

Well, that’s it. If you want to load our packs or any other 3rd party content, this is the only way to do it.

For advanced users, you can load packs from your computer to the Tyros wirelessly but we have found this to be unreliable, slow and generally hit and miss. Exporting to USB and loading from stick is much more solid and quicker.